## Slide 1: Ch.5. 산업활동과 오염
Past Activities Typically Conducted at Brownfields Sites | Typical Contaminants and Typical Sources
Agriculture | Volatile organic compounds (VOC); arsenic, copper, carbon tetrachloride, ethylene dibromide, and methylene chloride; pesticides; insecticides; herbicides; grain fumigants
Automotive refinishing and repair | Some metals and metal dust; various organic compounds; solvents; paint and paint sludges; scrap metal; waste oils
Battery recycling and disposal | Lead; cadmium; acids
Chloro-alkali manufacturing | Chlorine compounds; mercury
Coal gasification | Polynuclear aromatic hydrocarbons (PAH)
Cosmetics manufacturing | Heavy metals; dusts; solvents; acids
Dry cleaning activities | VOCs such as chloroform and tetrachloroethane; various solvents; spot removers; fluorocarbon 113
Electroplating operations | Various metals such as cadmium, chromium, cyanide, copper, and nickel
Glass manufacturing | Arsenic; lead
Herbicide manufacturing and use | Dioxin; metals; herbicides
Hospitals | Formaldehyde; radionuclides; photographic chemicals; solvents; mercury; ethylene oxide; chemotherapy chemicals
Incinerators | Dioxin; various municipal and industrial waste
Landfills—municipal and industrial | Metals; VOCs; polychlorinated biphenyl (PCB); ammonia; methane; household products and cleaners; pesticides; various wastes
Leather manufacturing | Toluene; benzene
Machine shops/metal fabrication | Metals; VOCs; dioxin; beryllium; degreasing agents; solvents; waste oils
Marine maintenance industry | Solvents; paints; cyanide; acids; VOC emissions; heavy metal sludges; degreasers
Munitions manufacturing | Lead; explosives; copper; antimony

## Slide 2
Paint/ink manufacturing | Metals (such as chromium, cadmium, lead, and zinc); VOCs; chloroform; ethyl benzene; solvents; paints; inks
Pesticide manufacturing | VOCs; arsenic; copper; pesticides; insecticides; herbicides; fungicides; xylene; chlorinated organic compounds; solvents
Petroleum refining and reuse | Petroleum hydrocarbons; benzene, toluene, ethylbenzene, xylene (BTEX); fuels; oil and grease
Pharmaceutical manufacturing | Lead; various organic chemicals; organic solvents
Photographic manufacturing and uses | Silver bromide; methylene chloride; solvents; photographic products
Plastics manufacturing | Polymers; phthalates; cadmium; solvents; resins; chemical additives; VOCs
Printing industry | Silver; solvents; acids; waste oils; inks and dyes; photographic chemicals
Railroad yards | Petroleum hydrocarbons; VOCs; BTEX; solvents; fuels; oil and grease; lead; PCBs
Research and educational institutions | Inorganic acids; organic solvents; metals and metal dust; photographic waste; waste oil; paint; heavy metals; pesticides
Scrap metal operations | Various metals (such as lead and nickel); PCBs; dioxin; transformers
Smelter operations | Metals (such as lead, copper, and arsenic)
Semiconductor manufacturing | Metals; VOCs; carbon tetrachloride; degreasing agents; solvents
Wood pulp and paper manufacturing | Chlorinated organic compounds; dioxin; furans; chloroform; resin acids
Wood preserving | Creosote; pentachlorophenol (PCP); arsenic; chromium; copper; PCB; PAHs; beryllium; dioxin; wood preservatives
http://www.ehso.com/contaminants.htm

## Slide 3
섬유산업은 가장 심각한 오염원 중 하나. 세계 은행에 따르면 산업 오염의 약 20% 정도가 섬유의 가공 및 염색에 기인함.
http://www.sustainablecommunication.org/eco360/what-is-eco360s-causes/water-pollution
http://www.theguardian.com/environment/2013/jan/04/mps-compensate-heavy-industry-carbon
Aerial view of the Tata steelworks at Scunthorpe
중공업에 의한 오염

## Slide 4
한 작업자가 (2009년 7월?) 중국 후베이성 관치아오(Guanqiao)호에서 죽은 물고기를 건져내고 있다. 더운 날씨가 처리되지 않은 산업 폐수와 겹쳐 약 50,000kg의 물고기를 죽였다. 가물, 인구 증가, 산업의 팽창 등이 심각한 물부족 상황을 야기하였다. 2009년 양쯔강의 수위는 1866년 이래 최저를 기록하였다. 이 때문에 제조업 및 하수 등으로 오염된 강 호수가 악화되었다. guardian.co.uk
http://bis402environment.blogspot.kr/p/water-2.html

## Slide 5
우리나라 대기 환경 기준
항 목 | 기 준 | 측정방법
아황산가스(SO2) | 연간평균치 0.02ppm 이하 24시간평균치 0.05ppm 이하 1시간평균치 0.15ppm 이하 | 자외선형광법 (Pulse U.V. Fluorescence Method)
일산화탄소(CO) | 8시간평균치 9ppm 이하 1시간평균치 25ppm 이하 | 비분산적외선분석법 (Non­-Dispersive Infrared Method)
이산화질소(NO2) | 연간평균치 0.03ppm 이하 24시간평균치 0.06ppm 이하 1시간평균치 0.10ppm 이하 | 화학발광법 (Chemiluminescent Method)
미세먼지(PM10) | 연간평균치 50㎍/㎥ 이하 24시간평균치 100㎍/㎥ 이하 | 베타선흡수법 (β­-Ray Absorption Method)
미세먼지(PM2.5) | 연간평균치 25㎍/㎥ 이하 24시간평균치 50㎍/㎥ 이하 | 중량농도법 또는 이에 준하는 자동측정법
오존(O3) | 8시간평균치 0.06ppm 이하 1시간평균치 0.1ppm 이하 | 자외선광도법 (U.V Photometric Method)
납(Pb) | 연간평균치 0.5㎍/㎥ 이하 | 원자흡광광도법 (Atomic Absorption Spectrophotometry)
벤젠 | 연간평균치 5㎍/㎥ 이하 | 가스크로마토그래프법 (Gas Chromatography)
http://www.me.go.kr/mamo/web/index.do?menuId=586

## Slide 6
우리나라 토양 환경 기준
  우려기준
    (정의) 사람의 건강 및 재산과 동․식물의 생육에 지장을 초래할 우려가 있는 토양오염의 기준
    (근거법령) 토양환경보전법 제4조의2, 같은 법 시행규칙 제1조의5
  대책기준
    (정의) 우려기준을 초과, 사람의 건강 및 재산과 동․식물의 생육에 지장을 주어서 토양오염에 대한 대책을 필요로 하는 기준
    (근거법령) 토양환경보전법 제16조, 같은 법 시행규칙 제20조
http://www.me.go.kr/mamo/web/index.do?menuId=586

## Slide 7
등 급 | 기 준 (㎎/㎏) |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | 카드 뮴 | 구리 | 비소 | 수은 | 납 | 6가 크롬 | 아연 | 니켈 | 불소 | 유기인 화합물 | P C B | 시안 | 페놀 | 벤 젠 | 톨루 엔 | 에틸 벤젠 | 크실 렌 | 석유계 총탄 화수 소 | 트리 클로로 에틸렌 | 테트 라클로로 에틸렌 | 벤조 (a) 피렌
1지역 | 4 | 150 | 25 | 4 | 200 | 5 | 300 | 100 | 400 | 10 | 1 | 2 | 4 | 1 | 20 | 50 | 15 | 500 | 8 | 4 | 0.7
2지역 | 10 | 500 | 50 | 10 | 400 | 15 | 600 | 200 | 400 | 10 | 4 | 2 | 4 | 1 | 20 | 50 | 15 | 800 | 8 | 4 | 2
3지역 | 60 | 2000 | 200 | 20 | 700 | 40 | 2000 | 500 | 800 | 30 | 12 | 120 | 20 | 3 | 60 | 340 | 45 | 2000 | 40 | 25 | 7
등 급 | 기 준 (㎎/㎏) |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | 카드 뮴 | 구리 | 비소 | 수은 | 납 | 6가 크롬 | 아연 | 니켈 | 불소 | 유기인 화합물 | P C B | 시안 | 페놀 | 벤 젠 | 톨루 엔 | 에틸 벤젠 | 크실 렌 | 석유계 총탄 화수 소 | 트리 클로로 에틸렌 | 테트 라클로로 에틸렌 | 벤조 (a) 피렌
1지역 | 12 | 450 | 75 | 12 | 600 | 15 | 900 | 300 | 800 | - | 3 | 5 | 10 | 3 | 60 | 150 | 45 | 2000 | 24 | 12 | 2
2지역 | 30 | 1500 | 150 | 30 | 1200 | 45 | 1800 | 600 | 800 | - | 12 | 5 | 10 | 3 | 60 | 150 | 45 | 2400 | 24 | 12 | 6
3지역 | 180 | 6000 | 600 | 60 | 2100 | 120 | 5000 | 1500 | 2000 | - | 36 | 300 | 50 | 9 | 180 | 1020 | 135 | 6000 | 120 | 75 | 21
우려기준
대책기준

## Slide 8
* 비 고
① 1지역 : 지적법에 의한 지목이 전․답․대․과수원․목장용지․광천지․대․학교용지․구거․양어장․공원․사적지
② 2지역 : 지적법에 의한 지목이 임야․염전․대․창고용지․하천․유지․수도용지․체육용지․유원지․종교용지
③ 3지역 : 지적법에 의한 지목이 공장용지․주차장․주차용지․도로․철도용지․제방․잡종지․국방시설

## Slide 9
토양 내 중금속의 근원(유래)
  암석(일반)
  광체
  오염
    다양한 점오염원 및 비점오염원
일반적인 암석 내 (중)금속 원소 함량
  고철질암 > 규장질암
  세립퇴적암 > 조립퇴적암
  유기물 함량이 높을 수록 높다
  인산염암 >흑색세일>세일>사암